## Slide 1: Machine Learning for Chip Design Automation
Mark Ren

## Slide 2: Outline
Introduction to design automation
Applications of ML for design automation
  Prediction: various ML models
  Generation
  Optimization
Conclusion

## Slide 3: Design Automation
Design Automation
Code
9B transistors
350 mm² die size
TSMC's 12FFN

## Slide 4: Design Automation Flow
RTL
Synthesis& DFT
Gate level netlist
Physical Design
Layout netlist
High Level Synthesis
SystemC
Design Spec
Functional Verification
Testability
Manufacturability

## Slide 5: Macro Trend 1: End of Technology Scaling
Moore’s Law: transistor count doubles every 1.5 – 2 years
  slow down and dead
Dennard scaling: P=CFV2, frequency scales exponentially as V drops
  Broken since 2005
How to improve design performance without technology scaling?
  Better design ideas
  Better design automation

## Slide 6: Macro Trend 2: Rising Design Cost
DARPA, ISPD 19
reduce design cost == improve design productivity => better design automation

## Slide 7: The Potentials of ML

## Slide 8
Can we use ML to improve design automation QoR and Productivity?

## Slide 9: ML for Design Automation
Prediction
Supervised Learning
Optimization
Reinforcement Learning
Generation
Unsupervised Learning
Notes: Purpose and scope, answer with the Quote
Improve -> purpose, not for fun
Scope is pretty big  anything learning through experience -> scope; look into details of the scope, there are three ways
Model a complex process as a black box and predict the outcome from features
Supervised learning: regression, SVM, RF, CNN, RNN, FCNN
Intelligently explore a large feature space to find the optimal target
Active learning, Bayesian optimization, Genetic algorithms, Reinforcement learning
Learn to generate a target directly from features
Generative models/Unsupervised learning: autoregressive, auto-encoder, GANs
Unsupervised, labels

## Slide 10: Prediction
Supervised Learning
  DRC Prediction with Classical Machine Learning method
  Power Prediction with Convolutional Neural Network (CNN)
  DRC Hotspot Prediction with Fully Convolutional Network (FCN)
  Testability Prediction with Graph Convolutional Network (GCN)

## Slide 11: Classical Machine Learning vs Deep Learning
Deep Learning
Machine Learning
Amount of Data
Performance
No need for feature engineering
https://arxiv.org/ftp/arxiv/papers/1803/1803.01164.pdf
Notes: First, let’s look at diference of classical ML and DL.
Classical ML has been applied to PD ….
For example, …
But deep learning can achieve … that is why
The other benefit … for example , the authors of
In this talk, I will focus …

## Slide 12: Congestion/DRC Prediction
RTL
Synthesis
Gate level netlist
Layout netlist
Placement
Optimization
Routing
Routing Congestion  DRC Violation

## Slide 13: Predicting DRC from Placement
Window based approach
Train SVM Classifier to identify DRC violation for each window
Collecting input features such as :
  Pin density, cell density
  Global routing resources
  Pin proximity
  Cell connectivity
  Net spreading …
Model
Routability Optimization for Industrial Designs at Sub-14nm Process Nodes Using Machine Learning, ISPD’17

## Slide 14: Predicting DRC from Placement
Results
SVM-based prediction
GR-abased prediction
Routability Optimization for Industrial Designs at Sub-14nm Process Nodes Using Machine Learning, ISPD’17

## Slide 15: Power Prediction
PRIMAL: Power Inference using Machine Learning (DAC’19)
Fast (1k-10k cycles/s)
Low Accuracy
Slow (10-100 cycles/s)
High Accuracy
Predict gate level power with RTL or SystemC register traces
SystemC
RTL
Gate Level Netlist

## Slide 16: Fast CNN
https://arxiv.org/pdf/1810.00736.pdf
ShuffleNet V2
Notes: The most successful DL model …
Many networks are developed…
This plot shows …
Generaly the higher the computing …
Let’s look at one of the efficient network …, inference speed of …

## Slide 17: Power Prediction with Fast CNN
PRIMAL: Power Inference using Machine Learning (DAC’19)
1
0
0
1
1
0
0
0
0
A
B
C
D
E
Reg-to-Pixel Mapping
0
0
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
C0: non-switching C1: 01
C2: 10
ShuffleNet V2
Fast & Accurate ML
1K – 50K inferences/s
Notes: Let’s look at a power prediction problem
Instead of extensive …., we would like a fast prediction …
To leverage well trained CNN netowkrs, we first ...
Then we apply the fast shufflenet on this image and replace …

## Slide 18: Power Prediction with Fast CNN
Register 160 384 405 438 381 372 5651 23531
& I/Os
DL has better accuracy than ML for large design
PRIMAL: Power Inference using Machine Learning, DAC’19
Notes: We compared CNN models with other …
Most models shows similar in small …
But on large design ….
We tried different reg-to-pixcel mapping, and found not much diffence, which indeed proves ….

## Slide 19: DRC Hotspot Detection
ROUTENET: Routability Prediction for Mixed-Size Designs Using Convolutional Neural Network, ICCAD’18
Input tensor constructed by stacking 2D features:
(1) Pin density, (2) macro (3) long-range RUDY, (4) RUDY pins
DRC Hotspot Map ?
Notes: We apply this network to predict DRC hotspot in thi joint work with …
Previous work is window based ML
In this work, features of the entire design image is used to predict hotspot.
Feaures include. …. And they are are mapped into channels of images,.
And the output is an image …

## Slide 20: Fully Convolutional Network (FCN)
Upsampling/Transposed Convolution
(Blue input, green output)
Fully Convolutional Networks for Semantic Segmentation, CVPR’15
No Fully Connected Layers
Notes: The second very popular …. Instead of predicting one…
The key difference is a upsampling …,
Most CNN layers keep the dimension, or reduce the …, upsampling actually increase the ….,

## Slide 21: ROUTENET Model
Pixel-wise loss function
ROUTENET: Routability Prediction for Mixed-Size Designs Using Convolutional Neural Network, ICCAD’18
Notes: Here is the detail of this model
Start with input feature maps, convolution, upsampling, shortcut …
Because the output is image , we can build cost function …

## Slide 22: DRC Hotspot Detection Evaluation
ROUTENET: Routability Prediction for Mixed-Size Designs Using Convolutional Neural Network, ICCAD’18
RouteNet
Ground True
Window-based ML
Notes: We compare the FCNN … ML window based
We can see ...

## Slide 23: Chip Testing
100010
000101
100111
011101
010101
101111
001011
110101
010101
101111
001011
110101
Input patterns
output patterns
golden patterns
?
Stuck-at-0 fault
GND
010101
111111
001111
110101
Notes: Not all the fautls can be easiy detected

## Slide 24: Testability Problem
i0
O
Almost always 0
B’s faults unobservable  Difficult-to-test (DT)
i1
i2
i3
i4
i5
i6
i7
i8
i9
i10
B
A
Almost always 0
B’s faults are observable with an inserted register
Test Point (TP)
Stuck-at-0 fault
GND
Notes: This the test point insertion problem

## Slide 25: Testability Prediction with ML
Given a circuit, predict which gate outputs are difficult-to-test (DT)
  Gate Features: [logic level, SCOAP_C0, SCOAP_C1, SCOAP_OB]
  Gate Label: DT (0 or 1) generated by TetraMax
Input Features
N1: 0,0,1,1
N2: 1,0,1,0
N3: 2,0,1,1
.
.
.
Output classification
N1: 0
N2: 1
N3: 0
.
.
.
ML Model
Notes: Due to the time limit, …
Unlike input features which can be obtained almost instantly, Take hours to get these labels
Predicting output classification from input node feature directly never going to work

## Slide 26: Graph Convolutional Network (GCN)
9
2
5
4
6
7
3
1
8
Aggregation (mean, sum)
Encoding (Rm  Rn,Relu)
Semi-Supervised Classification with Graph Convolutional Networks, ICLR’17
GCN aggregates information from neighboring nodes
Notes: Similar idea can be apply to graph as well, which is called GCN
Aggregates
Encoding

## Slide 27: GCN based Testability Prediction
Weighted sum & Relu(R4  R32)
Weighted sum & Relu(R32  R64)
1
0
1
0
0
0
Layer 1
Layer 2
Layer 3
Fully Connected Layers
Weighted sum & Relu(R64  R128)
(64,64,128,2)
  Logic Level SCOAP_C0 SCOAP_C1
  SCOAP_OB
High Performance Graph Convolutional Networks with Applications in Testability Analysis, DAC’19
Notes: We apply GCN to a ….
Simple intreoduction of testability problem
The input … three gcn layers, .. Fully connected, output

## Slide 28: Testability Prediction Accuracy
Chart: Testing Accuracy(%)
Chart: 
| Logistic regression | Random Forest | MLP | SVM | GCN
Precision | 0.641 | 0.631 | 0.764 | 0.663 | 0.91
Recall | 0.622 | 0.73 | 0.76 | 0.575 | 0.94
F1 score | 0.63136 | 0.6769 | 0.76199 | 0.61587 | 0.92476
Accuracy | 0.63 | 0.65 | 0.76 | 0.64 | 0.93
K: # GCN Layers
Test point insertion reduced by 11% over TetraMax.
Graph based model well-suited for EDA problems.
High Performance Graph Convolutional Networks with Applications in Testability Analysis, DAC’19
Notes: With this network, we achieved ….
Compared to classic machine learning …
we also see increasing accuracy when increasing …
Althought this is testability application, because physical design ….

## Slide 29: Generation and Optimization
OPC mask generation with Generative Adversarial Network (GAN)
Logic optimization with Reinforcement Learning

## Slide 30: Manufacturability Problem : Optical Proximity Correction (OPC)
Optical Proximity Correction (OPC)-Friendly Maze Routing, DAC’04

## Slide 31: Inverse Lithography Transform (ILT)
ILT very time consuming
Design target
Mask with OPC
Wafer
ILT

## Slide 32: Generative Adversarial Network (GAN)

## Slide 33: OPC-GAN
GAN-OPC : mask optimization with lithography-guided generative adversarial nets, DAC’18
Notes: One of the pioneering work in applying generative mode ….
In this work, the author trying to solve …
Tranditionally , opc mask is computed with …
In this work, they proposed to use …. Generator, discriminator …
It is more of an application of autoencoder

## Slide 34: Logic Optimization
Majority Inverter Graph (MIG)
Reducing logic depth with logic transforms
Deep Learning for Logic Optimization, IWLS’17
Complementary Associativity – Ψ.C
Associativity – Ω.A
Notes: Complementary Associativity
Assoicativity

## Slide 35: Reinforcement Learning Background
State : current screen
Reward : score you earned at current step
Action : move your board left / right
Policy : How to choose your action
Action value function : your predicted future total rewards

## Slide 36: Policy Gradient
Hung-Yi Lee, Deep Reinforcement Learning, 2018
Notes: Advantages:
Better convergence properties
Eective in high-dimensional or continuous action spaces
Can learn stochastic policies
Disadvantages:
Typically converge to a local rather than global optimum
Evaluating a policy is typically inecient and high variance

## Slide 37: Policy Gradient For Logic Optimization
Stochastic policy to select optimization transforms
Deep Learning for Logic Optimization, IWLS’17
RF Formulation
    Reward: logic depth reduction
    State: current graph, use GCN to learn graph state
    Action: which move to select
    Policy: compute probabilities of each move given a state
Notes: Complementary Associativity
Assoicativity

## Slide 38: Fruitful Design Automation Areas for ML Methods
Do not create a problem just for ML
Intractable or High Complexity
No Analytical Solution
Make Conventional EDA Algorithm Smarter
Really Hard Problems
Notes: What areas that traditional computation methods can not do well?
  High computation complexity
  No analytical solution
Examples
  Computation complexity: NP problems, Full Chip FinFET Self-heat Prediction
  Hardware correlation: System-level di/dt Noise Prediction for Test
  QoR prediction: DRC prediction at placement
  Design space exploration: HLS parameter tuning, circuit optimization, Neural architecture search
  Design flow productivity enhancement: Verification coverage enhancement
Make conventional EDA algorithm smarter
  Replace hand crafted heuristics: synthesis transform configuration, combinatorial optimization
Application of reinforcement learning and unsupervised learning in EDA have potential in the future
  Analog layout generation, verification, design generation

## Slide 39: Conclusions
Deep learning and machine learning can improve quality and productivity of design automation in many ways.
We should focus on innovative methods to apply advanced DL models to hard Design Automation problems
There are still a lot of challenges in applying DL : open dataset, transferability, interpretability